## Slide 1: Proposal for a correction to UN Regulation No. 51.03
Informal document GRBP-82-23 (82nd GRBP, 3-5 September 2025, agenda item 3)

## Slide 2: Scope
Annex 8 (Indoor testing) in Regulation 51.03 contains an inconsistency, as it refers to free-rolling tyre noise measurements being performed according to two different methods.
This document explores the issue and proposes a correction to resolve the inconsistency.

## Slide 3
R51.03 up to supplement 4 (introducing indoor testing Annex 8)
Annex 3
Methods and instruments for measuring the sound made by motor vehicles
3. Methods of testing
…
Indoor tests shall be performed according to paragraph 3.1. using the specifications of ISO 362-3:2016, variant A. For indoor application, the manufacturer shall provide to the technical service, documentation according to Annex 8, paragraph 1. Variant A is a combination of indoor testing (power train sound) and outdoor testing (tyre/road sound).
…
Annex 8 Indoor testing
Indoor testing is only for Annex 3 and Annex 7 measurements.
2. Vehicle tested indoor using Variant A
2.3. Tyre/road sound
The measurements of the tyre/road sound shall be performed on a test track as described paragraph 2.1.1. of Annex 3 of this Regulation. The evaluation of tyre/road sound consists of two procedures, namely:
Evaluation of free rolling sound;
(b) Evaluation of tyre/road sound including torque influence which can be derived from a) by a simplified method.
All conditions for evaluation of tyre/road sound shall be done according to paragraph 3. of this Annex.
3. Procedure for measurement, evaluation, and calculation of tyre/road sound when using variant A. All conditions for evaluation of tyre/road sound, free rolling sound, and torque influence are described in ISO 362-3:2016, Annex B.
ISO 362-3:2016 (Annex B)
Procedure for measurement, evaluation, and calculation of tyre/ road noise when using variant A (Annex B)
B.2.1 Tyre test vehicle
B.2.2 Power train conditions B.2.3 Tyre conditions B.2.4 Temperature correction B.3.1 Vehicle operating conditions for the free rolling noise component
ISO362-3:2016
Variant A: Measurement of power train noise on the dynamometer analogously to ISO 362-1 and energetical addition of the tyre/road noise (measured separately on an outdoor test track) (see 10.2).
All conditions for evaluation of tyre/road noise, free rolling noise, and torque influence are described in Annex B.

## Slide 4
Annex 3
Methods and instruments for measuring the sound made by motor vehicles
3. Methods of testing
…
Indoor tests shall be performed according to paragraph 3.1. using the specifications of ISO 362-3:2016, variant A. For indoor application, the manufacturer shall provide to the technical service, documentation according to Annex 8, paragraph 1. Variant A is a combination of indoor testing (power train sound) and outdoor testing (tyre/road sound).
…
Annex 8 Indoor testing
Indoor testing is only for Annex 3 and Annex 7 measurements.
2. Vehicle tested indoor using Variant A
2.3. Tyre/road sound
The measurements of the tyre/road sound shall be performed on a test track as described paragraph 2.1.1. of Annex 3 of this Regulation. The evaluation of tyre/road sound consists of two procedures, namely:
(a) Evaluation of free rolling sound; as described in Appendix 3 of Annex 3;
(b) Evaluation of tyre/road sound including torque influence which can be derived from a) by a simplified method.
All conditions for evaluation of tyre/road sound shall be done according to paragraph 3. of this Annex.
3. Procedure for measurement, evaluation, and calculation of tyre/road sound when using variant A. All conditions for evaluation of tyre/road sound, free rolling sound, and torque influence are described in ISO 362-3:2016, Annex B.
ISO 362-3:2016 (Annex B)
Procedure for measurement, evaluation, and calculation of tyre/ road noise when using variant A (Annex B)
B.2.1 Tyre test vehicle
B.2.2 Power train conditions B.2.3 Tyre conditions B.2.4 Temperature correction B.3.1 Vehicle operating conditions for the free rolling noise component
R51.03 up to supplement 7 (introducing tyre temperature correction
ISO362-3:2016
Variant A: Measurement of power train noise on the dynamometer analogously to ISO 362-1 and energetical addition of the tyre/road noise (measured separately on an outdoor test track) (see 10.2).
…
All conditions for evaluation of tyre/road noise, free rolling noise, and torque influence are described in Annex B.
Annex 3 – Appendix 3
Coast-by test method for measuring tyre-rolling sound emission
Comment: According to 2.3 a) the free rolling sound shall be evaluated according to Appendix 3 of Annex 3. However, 2.3 also states that the evaluation of tyre/road noise shall be done according to paragraph 3, which in turn points to ISO 362-3:2016 Annex B. The problem is that ISO 362-3 and Annex 3 of Appendix 3 provides different procedures to determine tyre/road noise!

## Slide 5: Background: Supplement 7
Submitted by the Informal Working Group on Measurement Uncertainties ECE/TRANS/WP.29/GRBP/2022/8
With the purpose to reduce test variability
Introducing:
Annex 3 – Appendix 2 “Correction for the tyre rolling sound component of pass-by sound measurements”
Annex 3 – Appendix 3 “Coast-by test method for measuring tyre-rolling sound emission
Introducing the following text in Annex 3:
3.4.2. Tyre rolling sound reference measurements according to Annex 3 Appendix 3 which are carried out independent of the type approval of a vehicle (see Case 2 of Annex 3 Appendix 2) are not mandatory but can be performed at the option and responsibility of the vehicle manufacturer.
and introducing the following text in Annex 8:
2.3. Tyre/road sound
The measurements of the tyre/road sound shall be performed on a test track as described paragraph 2.1.1. of Annex 3 of this Regulation. The evaluation of tyre/road sound consists of two procedures, namely:
(a) Evaluation of free rolling sound as described in Appendix 3 of Annex 3;

## Slide 6: Main differences between R51.03 and ISO362-3:2016
 | R51 Annex 3, app 3 | ISO362-3:2016
Purpose | To calculate the tyre rolling sound level at a reference temperature and speed, to correct test result in Annex 3. | To calculate tyre sound (rolling + torque) level as a function of vehicle position, which is added to indoor vehicle sound measurements
Speed at AA’ | 40-60 km/h Evenly distributed | 40-90 km/h 25-65 km/h (N3/M3) Incr. of 10 km/h
No of measurements. | ≥ 6 for the whole range | ≥ 4 per speed
Measurement read-out of sound level: | Maximum sound level | Continously between AA’ and BB’
Measurement read-out of speed | Front end of vehicle at line PP’ | Continously between AA’ and BB’
Type of test | Coast down (or constant speed for EVs) | Coast down
Tyres | Four tyres shall be fitted on the test vehicle | As fitted on the test vehicle
Torque model | No | Yes

## Slide 7: Summary
Supplement 7 introduced an inconsistency in R51.03 Annex 8. As currently written, it requires free-rolling tyre noise testing to be conducted in accordance with both ISO 362-3:2016 and Annex 3, Appendix 3
The test methods in ISO362-3:2016, and Annex 3, Appendix 3 are different and serve different purposes
Annex 3, Appendix 3 does not include a test method capable of generating a tyre sound model that can be integrated into indoor powertrain measurements.

## Slide 8: Proposal for a supplement
Annex 8
2.3. Tyre/road sound
The measurements of the tyre/road sound shall be performed on a test track as described paragraph 2.1.1. of Annex 3 of this Regulation. The evaluation of tyre/road sound consists of two procedures, namely:
(a) Evaluation of free rolling sound; as described in Appendix 3 of Annex 3;
(b) Evaluation of tyre/road sound including torque influence which can be derived from a) by a simplified method.
All conditions for evaluation of tyre/road sound shall be done according to paragraph 3. of this Annex.