## Slide 1: Report to 82nd Session of GRBP (September 2025)
IWG RD-ASEP Subgroup on UN-R 138 and UN-R 51
Submitted by the Chair of
IWG RD-ASEP Subgroup on UN-R 138 and UN-R 51
Informal Document GRBP-82-35
82nd GRBP, 03-05 September 2025
Agenda items 3 and 4

## Slide 2: IWG RD-ASEP Subgroup on UN-R 138 and UN-R 51
14
59
Number of Meetings
30th – 31st of October 2024 (hybrid in Berlin)
15th of November 2024 (virtual)
10th – 12th of December 2024 (hybrid in Tokyo)
17th of January 2025 (virtual)
30th of January 2025 (virtual)
13th of March 2025 (virtual)
8-10th of April 2025 (hybrid in Berlin)
30th of April 2025 (virtual)
5th of June 2025 (virtual)
6th of June 2025 (virtual)
18th of June 2025 (virtual)
8-11th of July 2025 (hybrid in Brussels)
6th of August 2025 (virtual)
2nd of September 2025 (hybrid in Geneva)
CPs: Canada, China (from 30/01/2025), EC (Chair), France, Germany, India, Japan, Netherlands, Switzerland, United Kingdom
NGO's: European Tuning Organization (ETO),ETRTO, IMMA, ISO, OICA (Secretary), World Blind Union (WBU)
1 individual expert
Participants (Contracting Parties & NGOs)

## Slide 3: Objectives of the subgroup
Subject: after two contradictory proposals for each regulation, at the 80th GRBP, it was agreed to find a satisfactory solution regarding the sound emissions of EVs and amend UN-R 51 and UN-R 138 accordingly
Timeline: working documents or, at least, informal ones were planned to be submitted to GRBP in September 2025 for both regulations (difficult to move on one without moving on the other as a satisfactory hand-shake is needed)
Due to extensive discussions, the documents should be submitted to the GRBP for February 2026

## Slide 4: Method and main orientations of the subgroup (1/2)
Discuss ideas and different options and their effects on safety and environment before drafting.
After the February 2025 GRBP the group focussed more on drafting the text and prioritize UN-R 51.
On UN-R 51: agreement on the introduction of EVs in the scope of Annex 7 (ASEP) and on the urgency to do so since some EVs are already equipped with external sound enhancement systems.

## Slide 5: Method and main orientations of the subgroup (2/2)
Justification and targets of UN-R 138
  The addition of a sound is justified by the safety issue created by the reduced audibility of quiet vehicles at lower speed.
  As this additional sound raises the sound level to which road users are exposed and has a direct impact on the environment, it should not be too loud.
Main orientations on UN-R 138
  On safety: agreement on the need to ensure an adequate level of safety (safety does not only rely on AVAS)
  On environment (as max SPLs are included in UNR 138):
    CPs emphasize the need to take advantage of the switch to EVs to diminish urban noise
    request from the industry to “keep agreeable flexibility in vehicle sound design where environment is not at stake”

## Slide 6: Progress on UN-R 51 (1/2)
It was decided to use the OICA proposal (working document GRBP/2025/29) as a basis for UN-R 51.
2 main points discussed on UN-R 51: addition of optional sounds and SPL limit lines for M1 and N1 EVs.
Agreements by the group on the addition of optional sounds:
  The requirements of UN-R 138 have to be fulfilled by the vehicles equipped with any sound system, including ESES.
  Need to avoid noise discontinuities that create annoyances
  Need to ensure that optional sounds reflects the expected sound of a vehicle.
  All electric vehicles shall comply with the requirements of Annex 7 due to the lack of methodologies to prove a vehicle without sound enhancement.

## Slide 7: Progress on UN-R 51 (2/2)
Additional comments still under discussion:
  It should be possible to switch optional sounds off and
  Optional sounds should be “off” when the vehicle starts
    Consequence: back-to back testing is possible to assess the level of optional sound (without any requirement at type approval stage)
To draw the limit line for M1 and N1 EVs, CPs have conducted a measurement campaign (information shared during February 2025 GRBP)
Data collected is available in an anonymized format on the wiki of the subgroup: SG_MD_05_0823_Measurement_Data_anonym.xlsx
Improvements since September 2024 GRBP
  the limit lines should be based on the speed of the vehicle (no more reference to the rpm)
  the limit lines should be as simple as possible

## Slide 8: Steps forward on UN-R 138 (1/2)
Identify and clarify all that needs to be clarified in the current text of UN-R 138:
  remove all the grey zones, e.g.:
    requirements applied to the AVAS sound or to the whole vehicle sound, what requirements in the AVAS fade-out speed range,
    the AVAS sound can be decreasing as the vehicle speed increases even in the mandatory speed range
  and clarify where the data introduced in the current text come from (to be able to know when an update is needed).
  Adapt in alignment with the changes to be made in UN-R 51, if needed.
Identify use-case scenarios in which safety or environment could be an issue and ensure the regulation tackles those cases

## Slide 9: Steps forward on UN-R 138 (2/2)
Need to ensure a good handshake with UN-R 51 regarding RD-ASEP
  the possibility to emit optional sound should not jeopardize safety
  limit at standstill is not in UN-R 51, this needs to be addressed
  ASEP (annex 7 of UNR-R 51) would only be for M1 and N1 vehicles
  The idea of having minimum SPLs in UN-R 138 for safety purpose and maximum SPLs in UN-R 51 for environmental purpose, needs to be discussed more in depth due to the difference in scope of both regulations.

## Slide 10: Thank you for your attention.