## Slide 1
Comment and Response to “ACPE-GTR-01-03”
Item list
ACPE-GTR-02-06

## Slide 2
UNR text no. | Word file Comment Summary | item | UNR Discussion results | justification | Reference document
1 1.1 | The applicable vehicle category (comfirmation) | Scope; vehicle category | M1/N1 | N1 accidents frequency is low, but after discussion both were included | ACPE-02-05 ACPE-09-03
5.1.4.1 (a) | Not clear relationship between AEBS and ACPE operations. | Relationship between AEBS and ACPE operations | When AEBS is activated, ACPE does not need to intervene | Accelerator operation may be an AEBS override operation. | ACPE-09-08
2.7 | Since there is no definition of the “Wall”, how should self-certification testing be conducted? | Definition of “Wall" | Set minimum size | There is no universal “Wall" Also, since it is not possible to guarantee operation on all “Walls" the manufacturer explains what kind of wall it works on. | ACPE-05-04

## Slide 3
UNR text no. | Word file Comment Summary | item | UNR Discussion results | justification | Reference document
5.2 5.2.1 5.2.2 | System OFF status (Display method, short-term / long-term) | OFF operation and display ・Short term OFF | Always displayed when the system is off | Set “off mode” considering the situation where it is necessary | ACPE-04-06 ACPE-06-07
 |  | OFF operation and display ・Long-term OFF | ・Operations with 2 or more actions ・Not always displayed when the system is off. | The situations where need to turn it off a long term are clear, and the display method was chosen to avoid annoyance. | 
5.1.4.1 (b) | Operation upper speed limit basis | Operating upper limit speed | 10km/h | Considering technical feasibility | ACPE-09-05
5.1.6.1 | Performance requirements | Speed reduction rate | 30% or more | “Collision energy” reduced by more than half | ACPE-04-10 ACPE-08-03