## Slide 1
Software updates and identification
  Implementation of Revision 8 to Consolidated Resolution No. 3 (R.E.3)
Informal document WP.29-197-24
197th WP.29, 11-14 November 2025
Provisional agenda item 2.3
Transmitted by the expert from France

## Slide 2: Background
Software updates
R156 provides requirements to ensure the safe management and deployment of software updates on vehicles that are already placed on the market.
Manufacturers must have processes in place to check if a software update affects type approved characteristics
If any approval to a UN Regulation is affected, the manufacturer must apply for an extension or a new approval before deploying the software update
All relevant UN Regulations must therefore accommodate software updates
Software identification
R156 gives a uniform standard for software identification called RXSWIN (Regulation No. X SoftWare Identification Number)
RXSWIN allows the quick identification of the exact approvals to all relevant UN Regulations where that software is involved
In parallel, identifying the exact software equipped on vehicles tested during approval is critical for traceability, as is already the case for the identification of hardware

## Slide 3: The amendments to R.E.3 (WP.29/2025/147)
Template for amending UN Regulations to:
Define RXSWIN
Allow manufacturers to apply for a new approval for purposes of software updates*
Not consider production as “definitely discontinued” if the manufacturer intends to obtain extensions for software updates
Include RXSWIN and related information on the communication form
AND
Require the exact software version of tested vehicles to be included in test reports
* when the original approval was extended to reflect new vehicles manufactured, and no longer corresponds to the technical characteristics of vehicles already on the market

## Slide 4: Which Regulations to amend?
Regulations where software is always involved
Example: AEBS
Regulations where software is sometimes involved
Example: underrun protection
Regulations where software is never involved
Example: external projections
Must be amended
Should not be amended
Criteria to be eligible:
UN Regulation applicable to vehicles of at least one category among M, N, O, R, S or T (Cat. L, components and STUs are not in scope of R156)
At least one requirement can be affected by vehicle software

## Slide 5: Provisional list of relevant UN Regulations
GR | UN Regulations
GRBP (see GRBP-79-42) | 51, 64, 138, 141, 142, 165
GRE (see GRE-90-27) | 10, 45, 48, 86
GRPE (see GRPE-91-07) | 24, 49, 68, 83, 85, 96, 101, 120, 154, 168
GRSG (see GRSG-130-42) | 18, 36, 39, 46, 52, 55, 58, 67, 73, 93, 97, 102, 105, 107, 110, 116, 121, 122, 125, 144, 147, 151, 158, 159, 160, 161, 162, 163, 166, 169, 176
GRSP (see GRSP-75-29) | 11, 12, 16, 17, 21, 32, 33, 94, 95, 100, 127, 134, 135, 137, 153
GRVA (see GRVA-18-34r1) | 13, 13-H, 79, 89, 130, 131, 139, 140, 152, 155, 156, 157, 171, 175, 178

## Slide 6: Call for action
GRs should amend their relevant Regulations as soon as possible to include the software-related provisions of Revision 8 to R.E.3
Amending the Regulations can be done via supplements: no new requirements
These amendments will allow OEMs to better implement R156, and will allow CPs to better trace and identify software on vehicles on the market after over-the-air updates are performed