## Slide 1: ETRTO comments on TA-37-5
TFTA 37th session part 2 26 August 2025

## Slide 2: ETRTO review of Regulatory text proposal TA-37-5
ETRTO reviewed the text proposal as per document TA-37-5, and has the following regulatory and technical comments.
Regulatory comments
5.1. is correct as it is.
XL and 3PMSF occurrences must be reviewed and replaced by the proper regulatory wording (reinforced or extra load and tyre for use in severe snow conditions)
Need to align wording, symbols and test reports for the two methods

## Slide 3
1. Regulatory comments (continued)
ETRTO tried to reword 12.6. in such a way that is does not refer to a specific date but rather to the date of application of the regulation by the CPs:
  12.6. Notwithstanding paragraph 12.5, Contracting Parties applying this Regulation and mandatorily requiring the approval pursuant to this Regulation shall continue to allow for a period of 24 months from the date of requiring the approval for all types of class C1 tyres the fitting on a vehicle in use of new class C1 tyres manufactured prior to the date of requiring the approval for all types of class C1 tyres and not type approved pursuant to this Regulation.
Or
  12.6. Notwithstanding paragraph 12.5, Contracting Parties applying this Regulation and mandatorily requiring the approval pursuant to stage 1 of this Regulation shall continue to allow for a period of 24 months from the date of requiring the approval for all types of class C1 tyres the fitting on a vehicle in use of new class C1 tyres that are manufactured prior to the date of requiring the approval pursuant to stage 1 for all types of class C1 tyres and that are not type approved pursuant to this Regulation.
With the possibility to extend it also to stage 2
  12.7. Notwithstanding paragraph 12.5, Contracting Parties applying this Regulation and mandatorily requiring the approval pursuant to stage 2 of this Regulation shall continue to allow for a period of 24 months from the date of requiring the approval for all types of class C1 tyres the fitting on a vehicle in use of new class C1 tyres that are manufactured prior to the date of requiring the approval pursuant to stage 2 for all types of class C1 tyres and that are not type approved pursuant to this Regulation.

## Slide 4
1. Regulatory comments (continued)
Annex 2. GRBP TFTA co-chairs eliminated the appendix subdivision. The result is that there are now many example1 and example 2 , so the reference to example 1 and example 2 aren’t anymore univocal.
Annex 3., table in 1.2.23., the definition of symbols T and R is not only useless but rather confusing: T is for temperature, not for candidate tyre, instead C is for candidate tyre
Annex 3. In general, the procedure for the choice of the candidate vehicle is confusing.
Annex 3, paragraphs 1.11.13.1. and 1.11.13.4.: find alternative wording for square fitment.

## Slide 5
2. Technical comments
About Invalid test results for vehicles with trouble
  Not agreed by ETRTO. Can create operational trouble, or impossibility to restart the test. No risk of cheating if the replacement vehicle is same model and same tuning, as the acceleration are constrained for the whole test for each vehicle.
  Proposal for 2026/02 GRBP
    delete or rewrite the text point C to clarify
    Add a constraint on maximal temperature variation between cand and ref when running missing part
Revise the wear level of SRTT17S
  JASIC proposal [50;190]  [45;190] mg/km/T for SRTT
  OK for 45 mg/km/T as minimum, should even go lower (e.g. 40 mg/km/T) when seeing RDE abrasion level values.

## Slide 6
Technical comments (continued)
About Mixed fitment method:
  ETRTO proposal made based on tests. Results will be available in TAPP file, and can be shown on TFTA 20250902
  About basis for determining the size to be tested on drive axle, proposal to add (in 2026/02) that the test report to tyre approval authority shall explain the vehicle choice
Front axle tuning (-1.2  -1.3 for camber)
  Camber has rather low impact on abrasion level. However, instead of adding -0.1 to the -1.2 without changing 0, ETRTO proposes to change [-1.2;0] to [-1.4; -0.2], so that the range is not increased, however is more realistic and taking into account actual vehicle market. As tuning range does not change, the accuracy does not change.
Rear axle tuning for RWD AWD vehicles
  Will be proposed in GRBP 202602

## Slide 7
Technical comments (continued)
TOE definition
  TOE data available in TAPP file for analysis. Can be refined if needed.
  Proposal of “Total TOE” recommended by test centers
  When different left and right TOE, compensation by driver using steering wheel to ensure staying on the road  half of total TOE on each wheel.
  ETRTO recommend to keep as proposed, allowed total TOE not increased by proposal  uncertainties not increased
Temperature ranges
  Y tyres: proposal based on COVA test results and rubber experts
  For other tyres, restricting temperature ranges allow to increase the method accuracy and be closer to real driving condition for these tyres  keep

## Slide 8
Technical comments (continued)
Reduction of minimal circuit length to 250 km instead of 300 km:
  To note that some existing circuit have an 8 shape, allowing battery loading during the shift.
  Risks (less representative, only 250 km in future, higher impact of circuit segment maintenance) seem acceptable. No data proving it would be wrong.
Additional clarifications on circuit surface definition:
  Yes, better to precise definition, roads have to be paved, and limited length of gravel (e.g. 10%)

## Slide 9: Thank you