## Slide 1: Proposal for amendments to UN R79 (Steering equipment)
Remote Control Parking (RCP)
Speed adjustment feature
Informal document GRVA-22-09
22nd GRVA, 24 June 2025
For review at the Bangkok meeting, hosted during the Road Safety week,
2-5 June 2025 (ESCAP/UNCC)
Provisional agenda item 6(b)

## Slide 2: UN R79 – RCP Safety improvement
The issue:
The system cannot distinguish whether the user is willing to initiate an emergency braking (by releasing the “button” of the remote-control device) or to bring the vehicle to a standstill without emergency.  As a result, the system must always perform an emergency braking.
Concept Idea:
Emergency braking takes place as today by releasing the “button” of the remote-control device.
Parking manoeuvres without emergency is made possible by the driver with an additional element of the remote-control device available to regulate the driving speed within the RCP operating range (SRCPmax) at a speed not higher than 10 km/h.
This allows a more precise and smoother operation, compared to the default behaviour of the system.
Safety Arguments:
Improved controllability by the driver
The driver can easily familiarize oneself with the function without generating useless emergency braking(s)
The driver can also bring the system to a standstill before the final state is reached and not with a sudden stop (e.g. to stop before being too close from a wall, for example).
The driver can prevent the sudden stop of the system in foreseeable situations.
5.6.1.2.1. The parking manoeuvre shall be initiated by the driver but controlled by the system. A direct influence on steering angle, value of acceleration and deceleration via the remote-control device or by the motion of the driver shall not be possible. A direct influence on the vehicle speed shall only be possible via the remote-control device within the defined operational conditions.
Now:
on/off
In future
+ (speed)
on/off
- (speed)
The implementation of such a “speed adjustment” feature, without changing the trajectory,
is a safety and comfort improvement.