## Slide 1: Proposals of Republic of Korea (on Emergency Door Opening)
EDO 2nd meeting
2025.09
Korea Automobile Testing & Research Institute
Jinseop PARK

## Slide 2: Background
Republic of Korea presented door opening issues with electrically activated doors during 76th GRSP session (GRSP-76-13-rev1)
Several GRSP experts expressed their support for the initiative during 77th GRSP session and the 1st meeting was virtually held on June 16th
Picture Source: GRSP-76-13-Rev1

## Slide 3: Discussion items on Emergency Door Opening
Evacuation from the inside - for electrically activated door system - for safety belt unbuckling
Rescue from the outside - door opening safety in case of power issue - door opening safety after collision - door opening safety with specific handle/system
Others - tailgate opening - submergence
* based on 2025 KNCAP protocol & GRSP comments, 1st meeting of interested GRSP experts

## Slide 4: Proposals of Republic of Korea – Priority 1
Door opening requirements with electricity supply cut off - amendment regulations: GTR No.1, UN R11 - test with a vehicle with its all related electricity supply cut off - doors shall be opened by main or emergency/secondary opening systems without any tools from inside and outside - the emergency/secondary opening systems shall be intuitive and those opening methods shall be described in the manual (incl. retractable case) - the intuitiveness requirements of the controller of those opening systems shall include at least the below · shall be clearly visible by the seated occupants (for interior) · shall not be hidden by any parts (e.g. covers, armrest, etc.) - further specific discussions needed (definitions, test conditions, etc.)

## Slide 5: Proposals of Republic of Korea – Priority 2
Door opening requirements after crash tests - amendment regulations: all crash test regulations (GTR No.14, UN R34, UN R94, UN R95, UN R135, UN R137, UN R153, & corresponding regulations) - test with a vehicle after crash tests (all doors except struck side doors in case of side crashes and tailgates) - doors shall be unlocked after crashes - door shall be opened when a pulling load is applied as below · hinged type doors: 750N or less · sliding type doors: 750N or less, 45 degrees (500mm opening) - further specific discussions needed (test conditions, etc.)

## Slide 6: Proposals of Republic of Korea – Priority 3
Other requirements for extrication - seat belt unbuckling after crashes (60N for frontal crashes, 100N for side crashes) - tailgate opening and vehicle submergence · agreed in principle · specific discussions needed from, especially, the testability perspective for self-certification compliance testing

## Slide 7
고맙습니다.
Thank you for your attention
jspark@kotsa.or.kr