## Slide 1: OICA Input to SLR-74 Topic: “Stop/DI Visibility”
3rd September 2025
SLR-74-08

## Slide 2: OICA Concerns with SLR-73-08 Rev.1
The SLR group is discussing German proposal to improve the visibility of direction indicators
Image: Copyright free
  German proposal from SLR-73-08 Rev.1:
5.7.1.3.3. If the distance between the edges of the apparent surfaces in the direction of the reference axis of the rear direction indicator lamp and the stop lamp is less than or equal to 25 mm,
(a) the area of the apparent surface of the rear direction indicator lamp up to a distance of 25 mm from the stop lamp shall be less than 25 per cent of its total apparent surface, provided that the geometrical visibility prescribed for the rear direction indicator lamp in 6.5.5. and the minimum photometric values according to the angle of light distribution are fulfilled without considering the area at the distance less than 25 mm from the stop lamp;
or
(b) the luminous intensity of the direction indicator should be at least 30% higher than the one of the stop lamp.
5.7.1.3.4. Appropriate evidence demonstrating compliance with the requirements indicated in paragraph 5.7.1.3.3. is provided in the test reports of the rear direction indicator.
OICA has concerns part (a). We believe it is not feasible to mask part of an apparent surface to confirm whether or not the minimum photometric values are achieved without considering the area <25mm from the stop lamp.

## Slide 3: OICA Concerns with SLR-73-08 Rev.1
So far, there is no study available, which states the uncertainty that is generated when determining the edge of an apparent surface.
Masking part of the apparent surface will be a manual process (most probably taping). Additional uncertainty is expected due to this operation which of course will influence the size of the part that remains to be measured.
It is assumed that blocking light within a distance of 25mm towards the stop lamp has to be done in the projection perpendicular to the reference axis (although it is not stated in the proposal).
The material used for blocking the light may have an influence, at least its back side regarding its reflectivity and the amount of light which is being scattered back into the device (and coming out at a different location).
There could be some practical issues if the stop and DI lamps are provided by different lamp manufacturers.

## Slide 4: Reminder of OICA Position for Discussion
There cannot be a problem when direction indicators meet one of the following criteria:
The apparent surface is equal to or greater than the apparent surface of the stop lamp.
The intensity at HV is a minimum of 25% greater than the intensity at HV of the stop lamp.
The separation distance in either the vertical or horizontal direction from the stop lamp is equal to or greater than 20 mm.
The apparent surface is equal to or greater than 30 cm².