## Slide 1: Proposal for an amendment of GTR No 20 – new requirements on thermal propagation
GRSP, 78th session, 02 December 2025
Prepared by EU on behalf of the IWG EVS
GRSP-78-19, submitted by EU
78th GRSP, 1-4 December 2025, agenda item 4

## Slide 2: 1. Process/objectives
16 meetings took places since 2018 / the adoption of GTR 20, with the work substantially affected by COVID pandemic.
Phase 2 efforts and discussions focused primarily on single-cell thermal runaway and propagation caused by an internal short-circuit. Canada, China, France, Germany, Japan, Republic of Korea, Netherlands (the Kingdom of), the United Kingdom of Great Britain and Northern Ireland, the United States of America, the European Union and OICA extensively exchanged information on the progress in thermal propagation research and field data.

## Slide 3: 2. Process/objectives
Two compliance paths were being developed by the IWG over the course of Phase 2. The first safety path is a physical test of vehicles or REESS and the second safety path was the risk management approach.
In October 2021, the informal working group established the thermal propagation task force (TP-TF), led by China, Japan, and Canada, and a thermal propagation documentation sub-group, led by the US.

## Slide 4: 3. Process/objectives
Between 2023 and 2024, the work of the Ad-hoc Special Interest Group on model regulation regarding the safety of electric vehicles with a focus on a thermal propagation test method, also laid an important foundation for the development of Phase 2 of the regulation.
Since 2024, several Contracting Parties adopted national / regional requirements on thermal propagation (UNR, FMVSS, GB). The initial objective was thus modified and Contracting Parties agreed to work on the common elements instead, and in a manner that this would not require any changes in their respective national / regional requirements.

## Slide 5: 4. Process/objectives
For the Contracting Parties electing to incorporate the test approach in their respective jurisdictions, there are 5 initiation methods.
For the Contracting Parties electing to pursue a risk management approach (RMA), the intent was to (1) document the known risk to vehicle occupants caused by thermal propagation which is triggered by an internal short-circuit leading to single cell thermal runaway, and (2) document the reduction of risk resulting from implementation of the identified risk mitigation functions or characteristics at the cell, REESS, or vehicle level.

## Slide 6: 5. Process/objectives
Although a part of the initial objectives, the IWG did not introduce new or amend the existing requirements from GTR 20 with respect to: water immersion test, long-term fire resistance test; REESS rotation test; REESS vibration profile; flammability, toxicity and corrosiveness of vented gas (i.e. quantification of venting for tests addressing safety of REESS post-crash, potential risk of "toxic gases" from non-aqueous electrolyte); post-crash REESS safety assessment and stabilization procedures; light electric vehicles; protection during AC and DC charging and feeding process; and overcurrent requirements.

## Slide 7: 6. Pending changes to the informal document
It is proposed to delete para 265, as it appears to be redundant after the adjustments of paras 263 and 264.
263. At the 22nd meeting of the Informal Working Group in October 2021, the Task Force on toxic gases (TP-TG), chaired by the EC, was established aiming at revisiting the adequacy of the visual inspection as a verification method for the occurrence of electrolyte leakage and venting. Experts from Australia, Canada, China, EU, India, Japan, Korea, USA and OICA have contributed to the work of the Task Force. Also, external independent specialists were invited to the TF-TG meetings and shared their research findings with the Task Force members. Thorough consideration has been given to various topics, including vented gas composition, toxic gas exposure thresholds, methods and techniques to detect and quantify venting and electrolyte leakage. Periodic progress reports on the work of TF-TG have been provided to the Informal Working Group (Related information: EVS24-E2TG-0101, EVS25-E2TG-0100, EVS27-E2TG-0100).
264. Given the fact that no sufficiently specific, accurate and robust method could be identified for the detection of venting and electrolyte leakage, the IWG recognised that more research is necessary to be able to conclude this topic (reflected in the 27th IWG meeting minutes, EVS27-A07). Hence, the decision was to retain the visual inspection as a verification method for the occurrence of electrolyte leakage and venting also in Phase 2 and to revisit the topic when more research data becomes available.
265. The IWG recognised that more research is necessary to be able to conclude this topic (reflected in the meeting minutes, EVS27-A07). Hence, the IWG decision is to retain the toxic gas provisions from Phase 1 also in Phase 2 and to revisit the topic when more research data becomes available. ]

## Slide 8: 7. Subject to agreement between the CPs
L. Recommendations
[279. With the adoption of the proposed amendments to GTR No.20, a comprehensive framework for electric vehicle safety has been created. Multiple Contracting Parties have already adopted national regulations consistent with the content of the amended GTR No.20 but the full implementation for many of these regulations will still be in the future. [Therefore, it is not yet possible to know the effectiveness of the amended GTR No.20 contents in addressing actual field safety incidents. ]
280. Further, the electric vehicle technologies continue to evolve including new lithium-ion chemistries, new chemistry families, new or enhanced battery diagnostic capabilities, higher power, energy and/or voltage system designs and so on. These technology advancements may impact what is an effective and appropriate safety regulation while it is not foreseeable as to which technologies will be adopted for commercial products. [The IWG efforts toward additional regulatory requirements would be severely hindered and likely result in premature and inappropriate regulation.] [new chemistries, protection scope, environments, etc.]
281. [Therefore, it is recommended that the IWG work on GTR No.20 be suspended, pending subsequent identification of emerging field safety needs. ]All Contracting Parties should monitor technology developments and the field safety of electric vehicles within their jurisdictions and report any emerging or potential issues to WP.29 or GRSP for consideration of re-initiating the IWG. Clear and specific terms of reference to define the scope and duration of the IWG work should be determined based on the actual field data and the assessment of the effectiveness of existing requirements in GTR No.20.
282. [Reserved for category L or micromobility] ]

## Slide 9: 8. Timeline
Informal discussion on the GTR 20 amendment proposal in GRSP in December 2025
Authorisation to start working on Phase 3 IWG EVS to be adopted in WP29 in March 2026
CPs/sponsors to agree on the final text proposal of the GTR 20 amendment by the end of Q1 2026
Final endorsement of the amendment of GTR 20 by GRSP in June 2026
Adoption of the amendment of GTR 20 by WP29 in November 2026