## Slide 1
Clarification of ESA charging conditions
(IWG-EMC-46-11/12 and IWG-EMC-49-07 Flowchart proposal Follow-up)
Proposal by CLEPA:
IWG-EMC-50-02

## Slide 2
Background & Rationale
Test Description | Vehicle |  | ESA | 
Broadband radiated emission | Annex 4 | Defined in a clear flowchart | Annex 7 | Not clearly defined
Radiated immunity | Annex 6 | Defined in a clear flowchart | Annex 9 | Not clearly defined
Emission of harmonics generated on AC power lines | Annex 11 | Defined in a clear flowchart | Annex 17 | Not clearly defined
Emission of voltage changes, fluctuations and flicker on AC power lines | Annex 12 | Defined in a clear flowchart | Annex 18 | Not clearly defined
Emission of radiofrequency conducted disturbances on AC or DC power lines | Annex 13 | Defined in a clear flowchart | Annex 19 | Not clearly defined
Immunity of Electrical Fast Transient/Burst disturbances conducted along AC and DC power lines | Annex 15 | Defined in a clear flowchart | Annex 21 | Not clearly defined
Immunity of surges conducted along AC and DC power lines | Annex 16 | Defined in a clear flowchart | Annex 22 | Not clearly defined
NOTE: The scope of this table is limited to test conditions relevant to REESS charging mode only.
A flowchart was added in R10.07 to clarify the charging mode configuration for vehicles.
However, such clarification is still not yet available for ESAs.
A proposal was submitted to introduce an ESA flowchart in UN R10.08. (IWG-EMC-46-11/12 and IWG-EMC-49-07)
The initial draft was a simplified AC/DC-based structure.
Based on feedback received, the approach was reviewed and updated to a MODE-based structure to align with the vehicle flowchart.
This ensures a clearer one-to-one alignment with the vehicle flowchart logic and avoids deviation caused by an AC/DC-only structure.
IWG-EMC-50-02

## Slide 3
ESA Flowchart Comparison
AC/DC-based (Initial Draft)
N
AC charging mode available?
Annex 7: test modes to be selected for REESS coupled to the power grid.
AC charging from standard socket-outlet?
Test at one reference charge current; it’s the supply path’s maximum rated input current.
Y
Y
AC charging from dedicated EVSE?
DC charging mode available?
Test the ESA in DC charging mode
Y
N
Test at one configuration (single or 3-phase) to be selected based on the maximum total nominal charge current
Y
End of test REESS coupled to the power grid.
N
N
Mode 1 available?
Mode 2
or 3 available?
Mode 2 available?
Test Mode1
Mode 3 available?
Test Mode3 in one configuration (single or 3-phase) to be selected based on the maximum total nominal charge current
Y
Y
N
Test Mode2
Y
N
Mode 4 available?
N
Test Mode4
Y
Y
End of test REESS coupled to the power grid.
N
N
Annex 7: test mode to be selected for REESS coupled to the power grid.
MODE-based (Proposed Revision)
IWG-EMC-50-02

## Slide 4
Proposal: Annex 7 Radiated Emission
Original flowchart (Vehicle)
Proposed flowchart (ESA)
Mode 3 test in one configuration (single or 3-phase) to be selected based on the maximum total nominal charge current
Mode 4 test with cable from the test facility
Mode 1 available?
Mode 2
or 3 available?
Mode 2 available?
Test Mode1
Mode 3 available?
Test Mode3 in one configuration (single or 3-phase) to be selected based on the maximum total nominal charge current
Y
Y
N
Test Mode2
Y
N
Mode 4 available?
N
Test Mode4
Y
Y
End of test REESS coupled to the power grid.
N
N
Annex 7: test mode to be selected for REESS coupled to the power grid.
Source : ECE/TRANS/WP.29/2025/110 - (GRE) - Proposal for Supplement 1 to the 07 series of amendments to UN Regulation No. 10 (Electromagnetic Compatibility)
IWG-EMC-50-02

## Slide 5
Proposal: Annex 19 Conducted Emission
Original flowchart (Vehicle)
Proposed flowchart (ESA)
Mode 3 test in both configurations (single and 3-phase), if available
Mode 4 test with cable from the test facility
Mode 1 available?
Mode 2
or 3 available?
Mode 2 available?
Test Mode1
Mode 3 available?
Test Mode3 in both configuration (single and 3-phase)
Y
Y
N
Test Mode2
Y
N
Mode 4 available?
N
Test Mode4
Y
Y
End of test REESS coupled to the power grid.
N
N
Annex 19: test mode to be selected for REESS coupled to the power grid.
Source : ECE/TRANS/WP.29/2025/110 - (GRE) - Proposal for Supplement 1 to the 07 series of amendments to UN Regulation No. 10 (Electromagnetic Compatibility)
IWG-EMC-50-02

## Slide 6
Proposal: Annex 9 Radiated Immunity
Original flowchart (Vehicle)
Proposed flowchart (ESA)
Mode 4 test with cable from the test facility
Mode 3 test in one configuration (single or 3-phase) to be selected based on maximum total nominal charge current
AC Mode available?
Mode 3 available?
Y
Y
N
Mode 4 available?
Test Mode4
Y
End of test REESS coupled to the power grid.
N
N
Annex 9: test mode to be selected for REESS coupled to the power grid.
Test Mode3 in one configuration (single or 3-phase) to be selected based on the maximum total nominal charge current
Test in only one AC Mode 1 or 2
Source : ECE/TRANS/WP.29/2025/110 - (GRE) - Proposal for Supplement 1 to the 07 series of amendments to UN Regulation No. 10 (Electromagnetic Compatibility)
IWG-EMC-50-02

## Slide 7
Proposal: Annex 17 Harmonics
Original flowchart (Vehicle)
Proposed flowchart (ESA)
2 For available charging modes on the vehicle with a maximum current ≤ 16A, the test shall be done either in Mode 2 or Mode 3 according to IEC 61000-3-2;
For available charging modes on the vehicle with a maximum current > 16A and <75A, the test shall be done only once either in Mode 2 or Mode 3 with a charging current > 16A according to IEC 61000-3-12.
Mode 1 available?
Mode 2
or 3 available?
Mode 2 available1
Test Mode1
Mode 3 available1
Test Mode3
Y
Y
N
Test Mode2
Y
N
N
Y
End of test REESS coupled to the power grid.
N
Annex 17: test mode to be selected for REESS coupled to the power grid.
1 For available charging modes on ESAs with a maximum current ≤ 16A, the test shall be done either in Mode 2 or Mode 3 according to IEC 61000-3-2;
For available charging modes on ESAs with a maximum current > 16A and <75A, the test shall be done only once either in Mode 2 or Mode 3 with a charging current > 16A according to IEC 61000-3-12.
Source : ECE/TRANS/WP.29/2025/110 - (GRE) - Proposal for Supplement 1 to the 07 series of amendments to UN Regulation No. 10 (Electromagnetic Compatibility)
IWG-EMC-50-02

## Slide 8
Proposal: Annex 18 Flicker
Original flowchart (Vehicle)
Proposed flowchart (ESA)
Source : ECE/TRANS/WP.29/2025/110 - (GRE) - Proposal for Supplement 1 to the 07 series of amendments to UN Regulation No. 10 (Electromagnetic Compatibility)
2 For available charging modes on the vehicle with a maximum current ≤ 16A, the test shall be done either in Mode 2 or Mode 3 according to IEC 61000-3-3;
For available charging modes on the vehicle with a maximum current > 16A and <75A, the test shall be done only once either in Mode 2 or Mode 3 with a charging current > 16A according to IEC 61000-3-11.
Mode 1 available?
Mode 2
or 3 available?
Mode 2 available1
Test Mode1
Mode 3 available1
Y
Y
N
Test Mode2
Y
N
N
Y
End of test REESS coupled to the power grid.
N
Annex 18: test mode to be selected for REESS coupled to the power grid.
Mode 3 test in one configuration (single or 3-phase) to be selected based on maximum total nominal charge current
Test Mode3 in one configuration (single or 3-phase) to be selected based on the maximum total nominal charge current
1 For available charging modes on ESAs with a maximum current ≤ 16A, the test shall be done either in Mode 2 or Mode 3 according to IEC 61000-3-3;
For available charging modes on ESAs with a maximum current > 16A and <75A, the test shall be done only once either in Mode 2 or Mode 3 with a charging current > 16A according to IEC 61000-3-11.
IWG-EMC-50-02

## Slide 9
Additional explanation – Harmonics & Flicker (1/3)
Key points from the 2025 Interpretation
IEC 61000-3-2:2018/AMD2:2024/ISH1:2025 (Interpretation Sheet + Amendment)
Background:
Some equipment indicates several different current values (e.g. “rated current” for different operating modes), which has led to inconsistent classification and occasional misapplication of IEC 61000-3-2(or 3)
Key principle:
If the equipment’s maximum continuous input current exceeds 16A, then the equipment should be tested under IEC 61000-3-12(or 11), and IEC 61000-3-2(or 3) should NOT be applied.
IEC 61000-3-3:2013/AMD2:2021/ISH1:2025 (Interpretation Sheet + Amendment)
- Reference standards
IWG-EMC-50-02

## Slide 10
Single- phase
AC supply only
supported?
End of test REESS coupled to the power grid.
Y
N
AC charging available?
Annex 17: test modes to be selected for REESS coupled to the power grid.
Imax in single- & 3-phase ≤ 16A
16A < Imax in single-phase ≤ 75A
& Imax in 3-phase ≤ 16A
16A < Imax in single & 3-phase ≤ 75A
Y
N
Test according to IEC 61000-3-2
in single or 3-phase at Imax
Test according to IEC 61000-3-12
in single-phase at Imax
Y
Y
Test according to IEC 61000-3-12 in the configuration (single or 3-phas) with the higher Imax
Y
N
16A < Imax in single-phase ≤ 75A
N
Y
N
16A < Imax in 3-phase ≤ 75A
N
Y
Test according to IEC 61000-3-12
in single-phase at Imax
Test according to IEC 61000-3-2
in single at Imax
Test according to IEC 61000-3-2
in 3-phase at Imax
Test according to IEC 61000-3-12
in 3-phase at Imax
Y
Y
N
Additional explanation – Harmonics & Flicker (2/3)
Supporting material (Vehicle footnote applied)
Single & 3-phase
AC supply
supported?
3- phase
AC supply only
supported?
Vehicle footnote 2
2 For available charging modes on the vehicle with a maximum current ≤ 16A, the test shall be done either in Mode 2 or Mode 3 according to IEC 61000-3-2;
For available charging modes on the vehicle with a maximum current > 16A and <75A, the test shall be done only once either in Mode 2 or Mode 3 with a charging current > 16A according to IEC 61000-3-12.
NOTE: Imax = maximum rated charging/input current
IWG-EMC-50-02

## Slide 11
End of test REESS coupled to the power grid.
Y
N
AC charging available?
Annex 17: test modes to be selected for Coupled to the power grid.
Imax in single- & 3-phase ≤ 16A
16A < Imax in single-phase ≤ 75A
& Imax in 3-phase ≤ 16A
16A < Imax in single & 3-phase ≤ 75A
Y
N
Test according to IEC 61000-3-2
in single and 3-phase at Imax
Test according to IEC 61000-3-2 in 3-phase
and IEC 61000-3-12 in single-phase at Imax
Y
Y
Test according to IEC 61000-3-2 in 3-phase at 16A if available
and IEC 61000-3-12 in single-phase at Imax
Y
N
16A < Imax in single-phase ≤ 75A
N
Y
N
16A < Imax in 3-phase ≤ 75A
N
Y
Test according to IEC 61000-3-2 in single-phase
at 16A if available
and IEC 61000-3-12 in single-phase at Imax
Test according to IEC 61000-3-2
in single at Imax
Test according to IEC 61000-3-2
in 3-phase at Imax
Test according to IEC 61000-3-2 in 3-phase
at 16A if available
and IEC 61000-3-12 in 3-phase at Imax
Y
Y
N
NOTE: Imax = maximum rated charging/input current
※ At 16A if available
= If the current consumption can be adjusted
This flowchart was drafted based on Remy’s (UTAC) comments and internal consideration; therefore, it may not fully reflect Remy’s exact intent.
However, it aims to capture the key principle raised by Remy:
one test to IEC 61000-3-2 and one test to IEC 61000-3-12 (one each)
Additional explanation – Harmonics & Flicker (3/3)
Supporting material (Remy’s comment considered)
Single & 3-phase
AC supply
supported?
Single- phase
AC supply only
supported?
3- phase
AC supply only
supported?
IWG-EMC-50-02

## Slide 12
Proposal: Annex 21 Burst
Original flowchart (Vehicle)
Proposed flowchart (ESA)
Mode 1 available?
Mode 2
or 3 available?
Mode 2 available?
Test Mode1
Mode 3 available?
Y
Y
N
Test Mode2
Y
N
Mode 4 available?
N
Test Mode4
Y
Y
End of test REESS coupled to the power grid.
N
N
Annex 21: test mode to be selected for REESS coupled to the power grid.
Mode 3 test in only one configuration, 3-phase if available.
Test Mode3 in only one configuration, 3-phase if available.
Mode 4 test with cable from the test facility
Source : ECE/TRANS/WP.29/2025/110 - (GRE) - Proposal for Supplement 1 to the 07 series of amendments to UN Regulation No. 10 (Electromagnetic Compatibility)
IWG-EMC-50-02

## Slide 13
Proposal: Annex 22 Surge
Original flowchart (Vehicle)
Proposed flowchart (ESA)
Mode 1 available?
Mode 2
or 3 available?
Mode 2 available?
Test Mode1
Mode 3 available?
Y
Y
N
Test Mode2
Y
N
Mode 4 available?
N
Test Mode4
Y
Y
End of test REESS coupled to the power grid.
N
N
Annex 22: test mode to be selected for REESS coupled to the power grid.
Mode 3 test in only one configuration, 3-phase if available.
Test Mode3 in only one configuration, 3-phase if available.
Mode 4 test with cable from the test facility
Source : ECE/TRANS/WP.29/2025/110 - (GRE) - Proposal for Supplement 1 to the 07 series of amendments to UN Regulation No. 10 (Electromagnetic Compatibility)
IWG-EMC-50-02

## Slide 14
MODE-based flowcharts are proposed to ESA charging-mode configuration.
This approach is applied to mirror the vehicle flowchart framework in UN R10.07, rather than re-structuring the logic into a AC/DC split.
For all relevant test items, the ESA flowcharts mirror the vehicle flowcharts as-is, while keeping the scope strictly ESA-only.
For Harmonics and Flicker, additional reference material is provided to further explain and demonstrate that the ESA flowcharts follow the vehicle flowcharts as-is, including how the applicable standards are determined by current rating and phase configuration.
Additional test conditions — such as charging currents above 75 A or new charging technologies — will be reviewed and incorporated once the corresponding standards are established.
Overall, the proposal aims to provide a clear, consistent, and harmonized configuration for ESA charging-mode testing, fully aligned with the UN R10.07 vehicle framework.
Summary and Outlook
The author and the speaker of this presentation confirm that they have authorization to use all content including photos and visual elements.
The material is either copyright-free or the author/speaker hold the necessary copyright or permission.
The UNECE will remove any material from its events and supporting websites if there is unlawful use of copyrighted material.
The author/speaker takes responsibility for any infringement on copyright and holds the UNECE harmless to this effect.
IWG-EMC-50-02