## Slide 1
WMG Safe Autonomy Research Group
Guidance proposal for AI Dataset Assessment for Automated Driving Systems
Prof Siddartha Khastgir CEng MIMechE
(WP.29/GRVA) Working Party on Automated/Autonomous and Connected Vehicles (23rd session)
22 September 2025
1
© WMG 2024
Informal document GRVA-23-34 23rd GRVA, 22-25 Sept. 2025, item 3

## Slide 2
Disclaimer:
Presentation at the views of WMG, University of Warwick, UK.
It doesn’t reflect the views of any of the contracting parties or the funder.
2
© WMG 2024

## Slide 3
Background
Artificial Intelligence (AI) forms a key building block of current and future Automated Driving Systems (ADS)
UN Regulation (UNR) and Global Technical Regulation (GTR) on Automated Driving System progressing to meet their mid-2026 timelines
Both UNR and GTR have limited focus on requirements for AI development and assurance
New Informal Working Group (IWG) on AI (AI-IWG) initiated: 1st meeting in August 2025
  Scope for the AI-IWG is broader than automated driving and covers wider AI applications in automotive
3
© WMG 2024
© WMG 2024
GRVA-23-34

## Slide 4
The Challenge
These activities fall short in providing engineering level guidance or measurable principles for authorities to assess the appropriateness of the AI used in the ADS’ performance
Any guidelines for AI development and assurance need to be technology agnostic
Every AI-based system will have the following development phases:
  Model creation
  Model training
  Model testing
Model training and model testing will require the use of “training” data and “testing” data,
Focus: Is the training and testing data / scenarios of the AI system sufficient?
4
© WMG 2024
© WMG 2024

## Slide 5
OASISS
© WMG 2025
5
Introducing OASISS
ODD-based AI Safety In autonomouS Systems
A methodology to quantitatively assess the adequacy of the training and testing datasets used on an AI model to ensure its safe deployment into its intended operating environment.

## Slide 6
Is the dataset complete with respect to the TOD?
OASISS in AI Safety Assurance
6
6
OASISS
Training Dataset
6
© WMG 2025
Testing Dataset
Is the dataset representative of the TOD?
Is the training and testing sufficient?
Representativeness
Completeness
Acceptability Argument
Are the deficiencies within the dataset acceptable for the considered TOD?
System ODD Specification
TOD Specification
(Operational Design Domain)
(Target Operational Domain)

## Slide 7
© WMG 2025
7
Extended Ontology
Representativeness
Completeness
Acceptability Argument
Guidance to the expected level of granularity
OASISS

## Slide 8
Is the dataset complete with respect to the TOD?
OASISS in AI Safety Assurance
8
8
8
© WMG 2025
Completeness

## Slide 9
“A scenario suite is complete with respect to the system’s area of deployment if it includes all operating conditions as they would occur within that area as well as those conditions that extend beyond the operational capacity of the system.”
9
© WMG 2025
Completeness

## Slide 10
© WMG 2025
10
Completeness
ODD
TOD
TOD
ODD
Condition | TOD | ODD
1 | In | In
2 | In | Out
3 | Out | In
4 | Out | Out
How would the system perform within its TOD?
How would the system perform outside its ODD?
Conditions in which vehicle will need to execute MRM
Conditions which are met by ODD
Conditions of interest for Completeness evaluation

## Slide 11
© WMG 2025
11
Scenario Level
Element Inclusion:
All parent attributes within TOD
Normal
Compact
Mini
Double
Roundabout
Walk
Run
U-Turn
Lane Change
Behaviour Inclusion:
All behaviours
Time Transition Inclusion:
All potential time transitions
Within each criteria, assigns a score of 1 if included and 0 if excluded

## Slide 12
© WMG 2025
12
Value Level
Assigns 1 if both within TOD and outside ODD conditions are met
Motor Vehicle
Car
Bus
Van
Truck
Amends the score of “Element Inclusion” – an indication that an element cannot be considered complete if its values are not specified
<2.5 mm/h
2.5 – 7.6 mm/h
7.6 – 50 mm/h
50 – 100 mm/h
>100 mm/h
Rainfall
Roundabout
Normal
Compact
Mini
Double
Categorical
Numerical

## Slide 13
© WMG 2025
13
Value Level
Assigns 1 if both within TOD and outside ODD conditions are met
TOD Requirement | ODD Specification | Candidate Scenario Suite Data | Completeness |  | 
 |  |  | In TOD | Out-of-ODD | In TOD ^ Out-of-ODD
Environmental Conditions |  |  |  |  | 
Wind [ 0 to 17.1 ] | Wind [ 0 to 20.7 ] | Wind [ 0 to 24.4 ] | 1 | 1 | 1
Scenery Elements |  |  |  |  | 
Drivable Area Type [ Motorway ] | Drivable Area Type [ Motorway ] | Drivable Area Type [ Motorway ] | 1 | 0 | 0
Special structure [ Bridge, Rail crossing, Tunnel ] | Special structure [ Bridge, Rail crossing ] | Special structure [ Bridge, Tunnel ] | 0 | 1 | 0
Dynamic Elements |  |  |  |  | 
VRU [ Cyclist, Motorcyclist ] | VRU [ Motorcyclist, Pedestrian ] | VRU [ Motorcyclist, Pedestrian ] | 0 | 0 | 0
Scenario Suite vs ODD
Scenario Suite vs TOD

## Slide 14
© WMG 2025
14
Micro-parameter Level
Amends the score of “Element Inclusion” after Value Level evaluation – an indication that an element cannot be considered complete if it its micro-parameters have not been considered
Roundabout
Number of exits
Central island features
Traffic control
Splitter islands
Vulnerable Road User
Clothing
Physical attributes
Objects
Mobility assist
Influential attributes
Within each element, assigns a score of 1 if associated micro-parameters are included

## Slide 15
Features | Completeness
In-TOD conditions | 
Out-of-ODD conditions (in & out-of-TOD) | 
Occurrence distribution comparison | 
Micro-parameters | 
15
© WMG 2025
Completeness

## Slide 16
OASISS in AI Safety Assurance
16
16
16
© WMG 2025
Is the dataset representative of the TOD?
Representativeness

## Slide 17
Representativeness
“A scenario suite is representative of the system’s area of deployment if the suite exhibits a distribution that is same or similar to that of real-world recorded data from that area at both individual element and joint element levels.”
17
© WMG 2025
Level 1
Level 2
Single distribution
Joint distribution

## Slide 18
© WMG 2025
18
Representativeness
How well would the system perform within its TOD?
ODD
TOD
TOD
ODD
Area of interest for representativeness evaluation
Condition | TOD | ODD
1 | In | In
2 | In | Out
3 | Out | In
4 | Out | Out
Conditions of interest for Representativeness evaluation

## Slide 19
© WMG 2025
19
Representativeness: Single distribution
Frequency of occurrence of individual elements
Driving studies
HD maps
Weather data
…
TOD data
Chart: Frequency of Rainfall
| Light | Moderate | Heavy | Violent
Series 1 | 20 | 28 | 12 | 3
TOD | 2 | 14 | 40 | 30
Scenario Suite | 6 | 18 | 38 | 35

## Slide 20
© WMG 2025
20
Representativeness: Joint distribution
Frequency of occurrence of elements with respect to other elements
Driving studies
Accident database
Insurance claims
…
TOD data
Chart: Frequency of Rainfall at Night
| Light | Moderate | Heavy | Violent
Series 1 | 20 | 28 | 12 | 3
TOD | 2 | 14 | 40 | 30
Scenario Suite | 20 | 28 | 12 | 3

## Slide 21
Features | Representativeness
In-TOD conditions | 
Out-of-ODD conditions (in & out-of-TOD) | 
Occurrence distribution comparison | 
Micro-parameters | 
Representativeness
21
© WMG 2025
Level 1
Level 2
Single distribution
Joint distribution

## Slide 22
OASISS in AI Safety Assurance
22
22
22
© WMG 2025
Acceptability Argument
Are the deficiencies within the dataset acceptable for the considered TOD?
Notes: Required to mention training or testing

## Slide 23
© WMG 2025
23
Acceptability Argument
The evaluation of the acceptability argument is subjective
As a model-agnostic framework, allows justification of any deficiencies that the Completeness and Representativeness evaluations detect, as what the framework considers as a “gap”, may be non-influential to that specific AI model’s performance - depending on its learning capacity.
Training scenarios are expected to be more tailored to the AI model’s requirements, which may result in deviations from real-world frequency occurrence distributions. This would automatically result in a lower representativeness score.

## Slide 24
© WMG 2025
24
Summary of the Concepts
Features | Completeness | Representativeness
In-TOD conditions |  | 
Out-of-ODD conditions (in & out-of-TOD) |  | 
Occurrence distribution comparison |  | 
Micro-parameters |  | 
e.g. ODD
Wind
0 to 24.4 m/s
Roundabout
Mini
Vehicle
Non-Motor Vehicle
VRU
Pedestrian, Motorcyclist
VRU
Pedestrian, Cyclist
Rainfall
0.01 to 100 mm/h
Wind
0 to 23 m/s
Roundabout
Mini, Compact
Vehicle
Motor Vehicle
e.g. London
21 mm/h
15 m/s

## Slide 25
© WMG 2025
25
Input dataset-related properties | Scenario suite-related properties
Accuracy | 
Completeness | 
Correctness | 
Independence of datasets | -
Integrity | -
Representativeness | 
Temporality | 
Traceability | 
Verifiability | 
OASISS Compliance with ISO PAS 8800
ISO PAS 8800
OASISS
OASISS framework aligns with ISO PAS 8800 by covering the following properties to address data insufficiencies:

## Slide 26
© WMG 2025
26
Current status
Paper on OASISS accepted at IEEE ITSC 2025
A paper detailing the proposed framework has been peer-reviewed and accepted for publication
Tool in Development: Actively developing a software tool to implement the framework in a usable and scalable form
Real-World Application:
The tool will be used on a real-world system to demonstrate its working
Citation: Jeyachandran et. al. (2025) Introducing OASISS : ODD-based AI Safety In autonomouS Systems. In: The IEEE International Conference on Intelligent Transportation Systems (ITSC), Gold Coast, Australia, 18-21 Nov 2025 (In Press)
Paper Open Access: https://wrap.warwick.ac.uk/id/eprint/192034/

## Slide 27
© WMG 2025
27
Next steps…
For AI model evaluation and assurance, it is key to undertake a dataset assessment for the training and testing data used as part of AI model development
Two key properties for assessment: Completeness and Representativeness of the dataset (with respect to TOD and ODD of the system)
UNR and GTR on Automated Driving System don’t cover such requirements at an engineering implementation level or measuring guidance for authorities
Need to consider the concepts of: Completeness; Representativeness and Acceptability Argument, as additional guidance for AI dataset assessment
OASISS provides a framework for engineering level guidance for developers and authorities providing quantified insights into the system’s trustworthiness for operation within that area

## Slide 28
Declaration:
The author and the speaker of this presentation (and companion document GRVA-23-25) confirm that they have authorization to use all content including photos and visual elements.
The material is either copyright-free or the author/speaker hold the necessary copyright or permission.
The UNECE will remove any material from its events and supporting websites if there is unlawful use of copyrighted material.
The author/speaker takes responsibility for any infringement on copyright and holds the UNECE harmless to this effect.
28
© WMG 2024

## Slide 29
Thank you.
warwick.ac.uk/wmg
@siddkhastgir
Siddartha Khastgir
WMG
University of Warwick
Coventry
CV4 7AL
United Kingdom
29
© WMG 2025
S.Khastgir.1@warwick.ac.uk