## Slide 1
Proposal for UN-R 10, 08 Series of amendments:
Precision of harmonics and flicker requirements
Supersedes: IWG-EMC-47-04 (OICA) Precision of charging condition and flicker requirements
March 2026
IWG-EMC-51-04

## Slide 2: Introduction
OICA proposes simplifications and clarifications of the measurement methods defined for
Harmonics requirements as given by the standards IEC 61000-3-2 and IEC 61000-3-12
Voltage changes, fluctuations and flicker requirement as given by the standards IEC 61000-3-3 and IEC 61000-3-11
Benefits of the proposal
Reduction of measurement time, but still covering the technical scope
Ensuring the measurements will be consistent between labs
Simplification of setup makes it possible to perform measurements in a regular test site
  Optional ground plane
  Shielded chambers do not need to be occupied for these tests
IWG-EMC-51-04

## Slide 3
Harmonics
Vehicle 7.3. (Annex 11)
ESA 7.11. (Annex 17)
IWG-EMC-51-04

## Slide 4: Precision of harmonics requirements
The objective of the requirements is to limit harmonic current injected to the public power mains grid in order to:
  reduce thermal aging of transformers and power lines, in particular the neutral conductor, and
  minimize interference with low‑frequency power line communication systems.
The measurement is performed over the frequency range from 50 Hz to 2000 Hz as a differential measurement on each phase.
Since the measurement is purely differential and does not use a ground reference, neither a Protective Earth (PE) nor a Ground Reference Plane (GRP) is required or specified in the basic measurement standard IEC 61000‑3‑2.
Furthermore, the basic measurement standard does not define a well‑specified measurement time that can be directly applied to vehicles; this aspect should be clarified.
Proposal overview:
  Clarify that the ground plane is optional, not required.
  Specify 10 minutes measurement time. Alignment with the proposed flicker observation time reduces testing complexity.
IWG-EMC-51-04

## Slide 5
Flicker
Vehicle 7.4. (Annex 12)
ESA 7.12. (Annex 18)
IWG-EMC-51-04

## Slide 6: Precision of flicker requirements
The objective of the requirements is to limit voltage fluctuations and flicker affecting the power mains grid, in order to
  limit flickering in lighting equipment, and
  stabilize the mains grid.
The measurement is performed as a differential measurement on each phase relative to neutral (N). The monitored phenomena have a low frequency character (typically < 10 kHz).
Since the measurement is purely differential and does not use a ground reference, neither a Protective Earth (PE) nor a Ground Reference Plane (GRP) is required or specified in the basic measurement standard IEC 61000‑3‑3.
Application of IEC-Standard: Annex A of IEC 61000-3-3 contains product specific instructions on limit application – but not for vehicles.
Proposal overview:
  Clarify that the ground plane is optional, not required
  Maintain cable length restriction
  Specify test conditions for vehicles in alignment with Annex A of IEC 61000-3-3:
    Measurement time (observation time) shall be 10 minutes. The measurement (observation) time shall be 10 minutes. This duration aligns with the default Pst measurement setting, is consistent with the proposed harmonics requirements, and reduces overall test complexity.
    Suppress the Plt requirement.
    Clarify that manual switching test are not required.
IWG-EMC-51-04

## Slide 7: Flicker requirements for other devices
 | Pst | Plt
Hair dryers and hair care devices |  | 
Multimedia equipment (without audio amplifiers) |  | 
Flow through heater |  | 
Audio amplifier |  | 
Air condition devices and industrial cooling devices |  | 
Welding equipment |  | 
Coffee and tea machines |  | 
Portable heating devices |  | 
Ventilators |  | 
IEC 61000-3-3:2013 + A1:2017 + A2:2021 + A2:2021/COR1:2022 Annex A
 | Pst | Plt
Cooking devices |  | 
Lighting equipment (only if switching is expected, not single light sources) |  | 
Washing machines |  | 
Laundry dryers |  | 
Cooling devices |  | 
Copying machines, printers |  | 
Vacuum cleaners |  | 
Blender |  | 
Tools without heating elements |  | 
Tools with heating elements |  | 
The voltage relative variation shall be measured in any case.
 Plt is only measured for devices with expected multiple switching action – no switching during charging of xEV expected.
IWG-EMC-51-04